## Slide 1: Undulator Preliminary Pulsedwire

## Slide 2: Keep trajectory straight…
I tuned trajectory in couple points to make straight.
Also, no reason not to adjust entrance/exit section at offsets if kick is giving too large waves on wire.
Initial post position:
  X1=2.250mm
  Y1=19.250mm
  X2=11.150mm
  Y2=9.750mm

## Slide 3: First iteration: xoffset, ytraj
Only measure -1000, 0, 1000 offsets.
Fit suggests adjustments:
  Dx1 = -900
  Dx2 = 550
New post positions:
  X1=1.350mm
  Y1=19.250mm
  X2=11.700mm
  Y2=9.750mm

## Slide 4: First iteration: yoffset, xtraj
Only measure -1000, 0, 1000 offsets
Fit suggests adjustments:
  Dy1 = 50
  Dy2 = 300
New post positions:
  X1=1.350mm
  Y1=19.300mm
  X2=11.700mm
  Y2=10.050mm

## Slide 5: Second iteration: yoffset, xtraj
Realized I made adjustments in wrong direction (sign error).
Adjusted dy2=-1000 and now results suggest no adjustment needed.
Can see effects of sag maybe?
Measured -1000, -500, 0, 500, 1000.
I preemptively correct the sign error in xoffset as well:
  Dx1 =1800
  Dx2 = -1100
New post positions:
  X1=3.150mm
  Y1=19.300mm
  X2=10.600mm
  Y2=9.050mm

## Slide 6: Second iteration: xoffset, ytraj
Measured -1000, -500, 0, 500, 1000.
Similar nonlinearity to yoffset, maybe this isn’t sag, just due to errors in calibration.
  I only adjusted entrance angle, so trajectory became quadratic at times.
Adjustments not worth making..
Final post positions:
  X1=3.150mm
  Y1=19.300mm
  X2=10.600mm
  Y2=9.050mm

## Slide 7: Final preliminary trajectories
text